## Slide 1
Control Room
2020
J.Hillairet

## Slide 2: Control Room (CR)
Control Room (aka "CR") is a graphical interface whose purpose is:
To plot various WEST database signals
  Does not (always) require to know the name of the diagnostic, signals are described with meaningful names
To plot WEST Session Leader plasma setup (aka “PCS waveforms”)
  Can plot previous pulse setups or “next pulse” setup (pulse number: 0).
The graphical interface organization can be personalized, saved and reopened later
To open Control Room, open a terminal and type:
  module load tools_dc
  CR

## Slide 3: Control Room graphical interface description
When you open Control Room, it is likely to appear like that
WEST Signals list
(can be hidden)
Plot zone
Pulse numbers
Download progress bar

## Slide 4: Control Room graphical interface description
Pulse numbers
Multiple « Tabs »
Multiple graphs (« Panels »)
The Graphical Interface can be personalized, (& saved/reopened)

## Slide 5
Graphical Interface Description

## Slide 6: Control Room graphical interface description

## Slide 7
“Tabs”.
A Tab contains one of few Panels
Tabs can be added, renamed and removed.
“Panel”.
Panel contains time-plot
Panels can be added and removed (vertically stacked)
Time-plot zone
Time-plot zone

## Slide 8
Pulse number(s) to plot (séparated by a comma « , »)
Convenient aliases:
0: next pulse (PCS waveforms only)
-1: last pulse
-2: before last pulse, etc.
Signal name selector (double click to select/deselect)
Double-click on a signal name will select it for plotting.
It is possible to select few signal names.
Selected signal naless appears in red.
Search zone, to search and filter a signal name
Signal type selector
“signals” (WEST database signals, from ARCAD (tsbase) and IMAS)
or
“PCS waveforms” (pulse configuration for the PCS)
It possible to superpose both kinds (but beware that the units does not always match
The selection zone can be resized or hidden (« Panels » menu)

## Slide 9
Examples of daily usage

## Slide 10: Control Room for the Engineer in Charge (EiC)
Control Room allows the EiC (but also all CR users) to check the next pulse settings
  Pulse settings are described by the Plasma Control System (PCS) waveforms
After the pulse, signals can be compared to PCS waveforms
EiC are in charge to check the Session Leader pulse setup, aka the “PCS waveforms”
Warning: the next pulse settings are not always available for reading! It depends of the IDPILOT sequence
Next pulse setting (pulse “0”) is only available during this time frame.
Once the pulse validated, the PCS .xml files are moved and hence no more accessible for reading.

## Slide 11: Example - SL to EiC : “on next pulse, I’ve reduced the prefill”
Comparing the previous pulse with the next pulse:
Prefill is generally made with the valve #7
(0 should be used here instead of 56439 in real situation)
SL comment:

## Slide 12: Example - SL to EiC : “on next pulse, I’ve increased plasma current and density”
Comparing the previous pulse with the next pulse:
(0 should be used here instead of 56441 in real situation)
SL comment:

## Slide 13: Example – Two gas injected during pulse
Impurity gas line #11 used for N2
SL comment:

## Slide 14: Example – SL to EiC: “I’ve increased the density envelope”
SL comment:

## Slide 15: Example – SL to EiC “I’ve moved the LPA 1cm further away”
SL setup the LPA radial position movement (∆R in mm)
  Can be compared post pulse with the achieved position (RLPA in meter)
SL comment:

## Slide 16: Example - Checking the cause of LH power reduction on a pulse
LH power is reduced is the Copper signal normalized to the core density (DSURVIE-SCU19/nl) exceeds a threshold (defined by the SL)
2 signals selected: LH1 & LH2 coupled powers
1 PCS waveforms & 1 signal selected:
Cu threshold
Cu signal normalized to central density
SURVIE signal exceeds defined Cu-level threshold few times
EiC comment

## Slide 17
Reporting Bugs

## Slide 18: I found a bug! How can I report it?
At least:
  Write me an email explaining the situation (and what should be the “normal” situation)
  If you can reproduce it: please list of the steps you’ve made, It always helps a lot.
Best:
  Do the same thing in the PPPAT bug tracker: https://github.com/IRFM/PPPAT/issues (requires github account, free)
  The bug tracker helps keeping traces and following bug resolution!